## Slide 1: DIGITAL DESIGN AND COMPUTER ORGANIZATION LABORATORY
UE19CS206
(0-0-2-1-1)
Computer Science and Engineering

## Slide 2: DDCO Lab: Tools / Languages
Department of Computer Science and Engineering
Icarus Verilog Simulator
GTKWave Waveform Viewer

## Slide 3: Verilog Program-Simple Circuit
DIGITAL DESIGN AND COMPUTER ORGANISATION LABORATORY
module simple_circuit (A, B, C, D, E);
output D, E; input A, B, C; wire w1;
and G1 (w1,A,B); // Optional gate instance name
not G2 (E,C);
or G3 ( D,w1,E);
endmodule
Department of Computer Science and Engineering

## Slide 4: Verilog Program-Simple Circuit
DIGITAL DESIGN AND COMPUTER ORGANISATION LABORATORY
// Test bench for Simple_Circuit_prop_delay module tb_simple_circuit;
wire D, E; reg A, B, C;
simple_circuit M1 (A, B, C, D, E); // Instance name required initial
begin
$dumpfile(“tb_simple_circuit.vcd");
$dumpvars(1,tb_simple_circuit); A = 1'b0; B = 1'b0; C = 1'b0;
#20
A = 1'b0; B = 1'b0; C = 1'b1; #20
A = 1'b0; B = 1'b1; C = 1'b0;
#D2e0partment of Computer Science and Engineering

## Slide 5: Verilog Program-Simple Circuit
DIGITAL DESIGN AND COMPUTER ORGANISATION LABORATORY
A = 1'b0; B = 1'b1; C = 1'b1; #20
A = 1'b1; B = 1'b0; C = 1'b0; #20
A = 1'b1; B = 1'b0; C = 1'b1; #20
A = 1'b1; B = 1'b1; C = 1'b0; #20
A = 1'b1; B = 1'b1; C = 1'b1; #20
end initial #200
$finish; endmodule

## Slide 6: Verilog Language Basics-Logic Gates
Lab Assignment 2-Simple Circuits
DIGITAL DESIGN AND COMPUTER ORGANISATION LABORATORY
A
C B
A2
C2 B2
B2 A2
Z
CIRCUIT 1
CIRCUIT 2
Y= [A2 OR (C2 AND B2)]OR(B2 AND A2)

## Slide 7: THANK YOU
TEAM DDCO
Department of Computer Science and Engineering